## Slide 1
Nested Interrupt Vector Controller
Lecture 3
Introduction to ARM Processor
This material is developed by IMTSchool for educational use only
All copyrights are reserved

## Slide 2
Definition of Exception
Exceptions are events which are generated asynchronously either from inside the core itself or from the external peripherals. In general any even that disturb the normal behavior of the processor is an exception.
Interrupts are used with exceptions from the external peripherals. In other words interrupt is nothing but an exception external to the processor core.
ARM Cortex M3/M4 Supports 255 exceptions
15 System Exception
240 Interrupts

## Slide 3
Nested Vectored Interrupt Controller
The Nested Vectored Interrupt Controller NVIC is an integrated part of the Cortex M3/M4 processor. It is closely linked to the CPU core logic and Its control registers are accessible as memory mapped. It provides the following features:
    Nested interrupt support
    Vectored interrupt support
    Dynamic priority changes support
    Reduction of interrupt latency
    Interrupt masking
The NVIC controls the interrupts as well as the system exceptions. The NVIC can be accessed in the System Control Space (SCS) address range, which is memory location 0xE000E000. Most of the interrupt control/status registers are accessible only in privileged mode, except the Software Trigger Interrupt register (STIR), which can be set up to be accessible in user mode.

## Slide 4
Nested Vectored Interrupt Controller
Processor Core
System Exceptions
NVIC
SysTick Timer
Cortex M3/M4 Processor
Peripherals
IRQn
NMI

## Slide 5
Interrupt Configuration
Each interrupt has a set of basic configurations through NVIC which are:
    Enable
    Clear Enable
    Set Pending
    Clear Pending
    Active status
    Priority level
. . . PRI0`
. . . IABR0
. . . CLRPEND0
. . . SETPEND0
. . . ICER0
. . . ISER0
0xE000E100
0xE000E180
0xE000E200
0xE000E280
0xE000E300
0xE000E400

## Slide 6
Enable Interrupt Register
Note
If a pending interrupt is enabled, the NVIC activates the interrupt based on its priority. If an interrupt is not enabled, asserting its interrupt signal changes the interrupt state to pending, but the NVIC never activates the interrupt, regardless of its priority.

## Slide 7
Enable Clear Enable Register
Note
Writing 1 to an ICPR bit does not affect the active state of the corresponding interrupt.

## Slide 8
Set Pending Register
Note
Writing 1 to the ISPR bit corresponding to an interrupt that is pending:
  – has no effect.
Writing 1 to the ISPR bit corresponding to a disabled interrupt:
  – sets the state of that interrupt to pending.

## Slide 9
Clear Pending Register
Note
A bit reads as 1 if the status of the corresponding interrupt is active or active and pending.

## Slide 10
Interrupt Active Bit Register
Note
A bit reads as 1 if the status of the corresponding interrupt is active or active and pending.

## Slide 11
Interrupt Priority
1- Define Number of Groups and Number of Sub Priorities

## Slide 12
Interrupt Priority
1- Assign a priority for each interrupt

## Slide 13
Stacking and Unstacking

## Slide 14
TAIL-CHAINING

## Slide 15
LATE ARRIVALS

## Slide 16
External Interrupt Controller

## Slide 17
This material is developed by IMTSchool for educational use only
All copyrights are reserved
www.imtschool.com
ww.facebook.com/imaketechnologyschool/